## Slide 1
01
PROBLEM STATEMENT
SENSOR SENTRY
A trust layer for any vehicle that navigates by GPS.
PS 18 · SPOOFING DETECTION & SENSOR FUSION
"Create an intelligent sensor-fusion system that cross-validates simulated sensor data to detect GPS spoofing, false readings, or manipulated environmental inputs."
GPS SPOOFING
An attacker fakes the satellite signal.
FALSE READINGS
No attacker — a sensor is simply failing.
MANIPULATED INPUTS
The world at the sensor is changed.
Three problems, not one. Most teams answer only the first. All three look alike at first, and they demand opposite responses.
where it really is
where GPS claims
residual 145 m
the witness — physics
the GPS claim — the lie
ALERT
guilty: gnss · attack
A spoofing walk-off as it happens: the real track, the position GPS claims, and the gap that gives the attack away.
01 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 2
02
PROPOSED SOLUTION
The vehicle has other senses. Nobody is asking them.
OUR ANSWER, IN ONE LINE
An attacker can fake the signal a vehicle receives. He cannot fake what the vehicle physically feels.
1
Build a second opinion
From its own motion, heading and wheels, the vehicle works out where it must be — without ever reading GPS.
2
Find who disagrees
Every sensor is checked against every other. If one disagrees with all the rest while they agree, that one is lying.
3
Attack, or breakdown?
A fault is random and messy. An attack is smooth, and pulls steadily one way. Drop the liar, keep navigating.
THE ONE QUESTION IT KEEPS ASKING
GPS says "you are here." Do the other senses agree? When they don't, that disagreement is the proof.
02 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 3
03
THE SENSORS · EVERY ONE, AND WHAT IT IS FOR
Six independent witnesses, all already fitted
Not one of these is new hardware. Every drone and every tracked truck already carries them.
GNSS
Global Navigation Satellite System
The satellite receiver — the one being lied to.
On the vehicle: antenna on the roof or airframe
an attacker can fake this
IMU · accelerometer
Inertial Measurement Unit
Feels every push, brake and bump — the vehicle's inner ear.
On the vehicle: a chip inside the tracker box
out of his reach
IMU · gyroscope
Inertial Measurement Unit
The same chip, measuring spin. It knows the moment the vehicle actually turns.
On the vehicle: the same chip as the accelerometer
out of his reach
BARO
Barometer — pressure sensor
Air thins as you climb, so pressure gives height.
On the vehicle: a vented port on the same board
only by physical means
MAG
Magnetometer — digital compass
Reads the Earth's magnetic field to know which way the vehicle points.
On the vehicle: away from the motors, often on a mast
only by physical means
ODOM
Wheel odometry
Counts wheel turns to measure real distance covered. Trucks only.
On the vehicle: the ABS sensor already at the wheel
out of his reach
The point of the last row: GPS is the only one an attacker can touch from a distance. The other five, he would have to reach the vehicle itself — which is the whole reason this works.
03 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 4
04
NAMING THE LIAR, AND KNOWING WHY
A diagnosis, not an alarm
imu
baro
mag
odom
gnss
disagrees with all four others
these four agree with each other
Four against one — that pattern is the accusation. If the compass were the odd one out, the compass would be named.
CAUSE 1 · A SENSOR FAULT
Random, jumpy, incoherent. Drop it, keep operating, flag the vehicle for service.
CAUSE 2 · A SPOOFING ATTACK
Smooth, steady, pulling one way. Too clean to be a fault. Alarm, switch navigation, preserve evidence.
CAUSE 3 · MANIPULATED ENVIRONMENT
One measurement shifts while the rest stay honest — the compass swings but the gyro felt no turn.
AND WHEN WE ARE NOT SURE
Below the confidence threshold we say unclassified. The system is allowed to say it does not know.
04 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 5
05
SYSTEM ARCHITECTURE
Three processes, all software, one laptop
simulator
our test tool
vehicle · sensors · attacks
detector
the product
cross-check · blame · classify
console
operator + phone
canvas map · no tiles
fleet service
cluster · zone · advisory
UDP :5005 · 20 Hz
no truth crosses here
WS :8080 · 20 Hz
verdicts + trust
WS :8081 · incidents
HTTP :5010 · start · reset · inject attack
The rule the whole demo rests on: the simulator and the detector are separate processes, and no ground truth ever crosses the socket — no true position, no attack flag, nothing. The detector is structurally incapable of cheating.
05 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 6
06
NOVELTY
Four things that make this ours
The novelty is not in noticing that GPS can be faked — it is in where the defence sits, and what it does once it fires.
01
No hardware at all
Today's protection is an anti-spoofing antenna fitted per vehicle. It protects the fleet you buy next year. Ours protects the fleet running today.
02
It names the guilty sensor
Not "something is wrong" — "the compass is lying, and the other four agree that it is." That difference decides whether the operator can act.
03
Attack or fault — the question everyone skips
Others stop at "anomaly detected." We answer why, because a broken sensor and a deliberate attack demand opposite responses.
04
The fleet checks itself
One vehicle might be a fault. Four in the same area at the same moment is certainly an attack — and you know where the attacker stands.
Claim 04 is also the business. Every vehicle added is another witness on the map. A competitor can copy our code in a month. They cannot copy the fleet.
06 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 7
07
WHAT WE CAN EXPECT
What the finished system will do — and where it fails
hidden inside our own drift
0
2
4
6
8
1.18
0.0
1.18
0.2
1.29
0.5
1.79
1.0
3.09
2.0
7.24
5.0
spoofing walk-off speed (m/s) · y = residual ÷ the uncertainty we claim
Measured on our own detector. Below about 0.2 m/s a spoofer moves us slower than our own drift, and we miss it.
1
Spoofing caught, GPS named
and the vehicle stays on its true route afterwards.
2
Zero false alarms
a clean run with hard turns finishes with no alerts.
3
A broken sensor is called a fault
not an attack. Different symptom, correct diagnosis.
4
A magnet is called interference
the compass swings, the gyro felt no turn.
5
Two liars → "I don't know"
it returns cannot_isolate, not a confident wrong answer.
6
Four vehicles → one attack zone
one alone produces no circle.
7
Trucks by configuration only
switching vehicle type changes settings, not code.
8
Every incident replays exactly
the stored record reproduces an identical verdict.
07 / 09
SENSORSENTRY · PS 18 · REVIEW 1

## Slide 8
08
IN CLOSING
An attacker can fake the signal.
He cannot fake what the vehicle feels.
NO HARDWARE
Ships as a software update into fleets already on the road today.
A DIAGNOSIS, NOT AN ALARM
Names the lying sensor, and says whether it is an attack or a breakdown.
HONEST ABOUT ITS LIMITS
It says cannot_isolate when it does not know, and we show you where it fails.
AND WHERE AN AI MODEL IS ALLOWED TO SIT
Nothing in the detection path calls an AI model. It earns exactly one job: writing the incident report after the event, behind a visible on/off switch. Turn it off, re-run the attack: detection is identical.
08 / 09
SENSORSENTRY · PS 18 · REVIEW 1